## Slide 1: State of the Art in Remote Monitoring of Implantable Devices
Prof. Dr. THOMAS DENEKE
Heart Center Bad Neustadt
Bad Neustadt, GER

## Slide 2: Heart Center Bad Neustadt (NES)

## Slide 3: NES
Bad Neustadt

## Slide 4: Rhoen: UNESCO biosphere reserve

## Slide 5: Le telecardiogramme, 1906
1st ECG transmitted via telephone line by
W. Einthoven
Einthoven; Arch Internat Physiol 1906

## Slide 6: Introduction: Remote monitoring
Capability of devices to connect wirelessly and distribute data has revolutionized cardiac device care
Remote monitoring (RM) - as a non-active act of continuous monitoring of cardiovascular health-related parameters - very helpful in rural/remote areas with long patient travel distances
RM-capable devices in cardiovascular health:
Implantable active cardiac devices (PM, ICD, CRT)
Implantable cardiac monitors (ILR, implantable hemodynamic sensors)
Wearable cardiovascular monitors (watches, wristbands, textiles)

## Slide 7: AGENDA: State of the Art Remote Monitoring
How does it work?
Effects on in-patient visits and time-to-event detection
Detection of atrial fibrillation (AF)
Effects on ICD-shocks
Effects on mortality?

## Slide 8: Remote monitoring (RM)
automated transmission of data provided by the device including daily self-testing and event notification for out-of-bound parameters and patient specific events: device- and biological/disease-monitoring
no interaction from patient needed, easy to install
Notes: Embedded technology has createdthe ability of the device to monitor their own funciton, record arrythmias and other physiological paramters and communicate this information to health care providers

## Slide 9: Remote monitoring in CIEDs
RM may document same data as IPE – 2 different sets of events:
technical events / device related – technical device integrity
patient events / disease affected – biological/disease parameters
Aprox 20% of CIED pts not in person seen for follow-up within first 12 months after implant
Need for structured regular follow-up but in-person evaluations (IPE) has failed to engage many pts (specifically those with long travel distances and need to take off time from work)
Remote monitoring technology developed as complementary to IPE and to replace some of routine follow-up
Up to 80% of implanted PM, ICDs and CRTs have availability of RM, actively used in aprox. 40% of these pts

## Slide 10: RM of active CIEDs (PM, ICD, CRTs)
Overall complications in ICD pts during FU: 9.1% (6.4 to 12.6%)
Lead related: 5.8% including displacement (3.1%)
Generator related: 2.7%
Ezzat et al. Open Heart 2005; Schuchert et al., Europace 2013
CRT-D patients:
Lead related: 9.2% - mostly related to LV-lead
 all detectable via remote monitoring/remote interrogation
Incidence of device events increases with complexity of device

## Slide 11: Case # 1: Device surveillance
 ICD-lead dysfunction
67 year old male patient
remote myocardial infarction - EF 23% - QRS 80 ms, SR
ICD Implantation - single chamber ICD (MADIT II)
16 months of uneventful follow-up
then: alert by telemonitoring due to frequent non-sustained VF-episodes

## Slide 12
Remote monitoring: proven effects
Proven early detection of relevant clinical events, reduces time from event to clinical action (TRUST, CONNECT, ECOST)
High reliability of transmissions (TRUST)
Reduction of follow-up burden (TRUST, COMPAS, REFORM) compared w/ standard of care
Proven reduction of hospitalization due to AF and of related strokes
Proven reduction of inappropriate ICD-Shocks (ECOST)
Varma et al., Circ 2010; Mabo et al., Eur Heart J 2012; Guedon-Moreau et al, Eur Heart J 2012; Hindricks et al., Eur Heart J 2014
> 400 published manuscripts incl. 7 RCTs on effects of RM

## Slide 13
Remote monitoring: proven effects
Proven early detection of relevant clinical events, reduces time from event to clinical action (TRUST, CONNECT, ECOST)
Proven reduction of ICD-Shocks (ECOST)
Proven reduction of hospitalization due to AF and of related strokes
Reduction of follow-up burden (TRUST, COMPAS, REFORM) compared w/ standard of care
High reliability of transmissions (TRUST)
Varma et al., Circ 2010; Mabo et al., Eur Heart J 2012; Guedon-Moreau et al, Eur Heart J 2012; Hindricks et al., Eur Heart J 2014
> 400 published manuscripts incl. 7 RCTs on effects of RM
the twin epidemics: AF and chronic HF
 in these pts RM must be considered gold standard

## Slide 14
Varma et al., Circulation 2010
1339 pts with Lumos-T
automatic daily RM surveillance
3-mo IPE
R
Follow-Up 12 mo
 | RM | conventional
Primary prophylaxis ICD | 72.2% | 73.8%
CAD | 64.8% | 71.7%
Dual-chamber ICD | 57.8% | 56.6%
102 US centers
2005 to 2008
Remote monitoring: proven effects

## Slide 15: RM: Effect on time to event identification
 | RM | Conventional | p
3-mo IPE visits adherence | 93.5% | 88.7% | <0.001
Mean IPEs | 2.1 | 3.8 | <0.001
Unscheduled visits | 0.78 | 0.50 | 0.009
12-mo survival | 96.4% | 94.2% | 0.174
Time from event-onset to evaluation (AF, VT, VF) | 1 day | 35.5 days | 

## Slide 16: RM: Effect on follow-up burden
Comparing RM to conventional IPE at 3 to 6mo (ICD pts)
RM allows to reduce IPEs by 45%
RM reduces time-from-clinical-event-to-clinical-decision/action
Varma et al., Circulation 2010; Crossley et al., JACC 2011
Notes: 12 mo Follow-up (TRUST, CONNECT) or even 24mo (ECOST)

## Slide 17: Today: technical & physiological data
<<<<<<<<
physiological parameters
Notes: Comprehensive reporting of technical and physiological/disease specific parameters

## Slide 18: The Twin Epidemics: AF and HF
Previosly unrecognized AF in between 30 to 60% of ICD pts
risk of thrombembolic complications significantly increased in episodes > 24hrs
90% of AF episodes triggering device alerts asymptomatic
RM detects AF 1 to 5 mo earlier compared to standard protocol
early AF/AHRE detection  may avoid inappropriate ICD-interventions, heart failure, loss of biventricular pacing, enables early onset of OAC
Eur Heart J 2017; Orlov et al., PACE 2007; Bunch Heart Rhythm 2009

## Slide 19: RM: Effect on inappropriate shocks
early detection of AF with rapid V-conduction, T-wave oversensing, device malfunction may help to reduce unnecessary ICD shocks
ECOST study: randomized, prospective, multicenter ICD-trial
Guedon-Moreau et al.; Eur Heart J 2012
RM reduces inappropriate but not appropriate ICD-shocks

## Slide 20
Hindricks et al., Lancet 2013
664 pts with DDD-ICD or CRT-D
NYHA II or III
333 RM
331 control
63 pts (18.9%)
90 pts (27.2%)
12-mo: worsened clinical status
p = 0.013
RM: Effect on mortality
R
Notes: BIOTRONIK Home Monitoring enabled >30% reduction of worsening of clinical status.
Modified Packer Score
Patients are classified as “worsened” in case of:
Death
Overnight hospitalization for worsening heart failure
Worsening in NYHA Class
Deterioration in patient’s global self assessment

## Slide 21
RM: Effect on mortality
Hindricks et al., Lancet 2013

## Slide 22: RM: Effect on mortality
Parthiban et al., JACC 2015
OR for mortality with RM was not different from in-office follow-up (control) (OR: 0.83; 95%-CI: 0.58 – 1.17; p=0.285)
only IN-TIME reported significant reduction in overall mortality
7 Randomized Controlled Trials (RCTs) report on mortality comparing remote monitoring to conventional follow-up (4.932 pts total)
Notes: Reasons for differences: 1. daily transmission, 2. complete set of HF data evaluated, 3. predefined set of action-events

## Slide 23: RM: Effect on mortality
Parthiban et al., JACC 2015; Morgan et al., Eur H J 2017
OR for mortality with RM was not different from in-office follow-up (control) (OR: 0.83; 95%-CI: 0.58 – 1.17; p=0.285) in 7 RCTs
only IN-TIME reported significant reduction in overall mortality
8 Randomized Controlled Trials (RCTs) report on mortality comparing remote monitoring to conventional follow-up (6.582 pts total)
1 recent RCT including 1650 pts showed no benefit of weekly RM using single parameter HF monitoring
Primary Endpoint (death or CV hospitalization) occurred in 42.4 vs. 40.8%
Notes: Reasons for differences: 1. daily transmission, 2. complete set of HF data evaluated, 3. predefined set of action-events

## Slide 24: Differences in RM systems
Differences in RM portals: daily transmission, multiparameter set of HF-data vs vs. single parameter, pre-defined set of action-events

## Slide 25: Mortality reduction and mode of RM
-5.3
0.3
-1.5
-1.9
in Biotronik remote monitoring trials: 1.9% absolute reduction of all-cause mortality (p=0.037)
 | IN-TIME | ECOST | TRUST
Site selection | 26 sites in Germany + 10 other sites | 43 sites in France | 102 sites in USA
Patients included | 664 | 414 | 1327
Dual-chamber ICD | 274 (41.3) | 123 (29.7) | 765 (57.6)
CRT-D | 390 (58.7) | 0 (0.0) | 0 (0.0)
daily RM reduces mortality in a broad spectrum of ICD-pts

## Slide 26
% BiV pacing
RM: disease specific events - HF Monitor
Biological monitoring/monitoring of disease state:
Multiparameter Heart Failure Monitor - overview of clinical HF parameters
Parameter | Worsening HF
Pt activity | 
AF burden | 
V-rate during AT | 
% BiV pacing | 
HR variability | 
Mean HR | 
Set of RM parameters relates to disease state

## Slide 27: RCT and mortality – daily RM
All-cause mortality
All-cause mortality or
WHF hospitalization
38%
36%
Clinical endpoint
(at 12 months)
relative risk reduction
1.9%
5.6%
absolute risk reduction
p<0.05
p<0.01
Daily transmitting RM is associated with a significant reduction of all cause mortality and combined endpoints
Clinical benefit mainly driven by prevention of heart failure exacerbation

## Slide 28
Case # 2: Heart Failure Worsening
Male Pts, ICM, EF 28%, LBBB-QRS = 170ms
no hx of atrial arrhythmia
primary prophylaxis ICD
12/2016 CRT-D (Iforia 5 HF-T)

## Slide 29
Case # 2: Heart Failure Worsening
Pt increased dyspnea, specifically on exertion
daily RM indicated onset of AF (first diagnosis)
OAC was initiated
Cardioversion with early relapse
AF ablation was performed
atrial arrhythmia
burden
pt activity/d
mean heart rate
% biv pacing
thorax impedance

## Slide 30
Case # 2: Heart Failure Worsening
atrial arrhythmia
burden
pt activity/d
mean heart rate
% biv pacing
thorax impedance

## Slide 31: Implantable Loop Recorders
15% of strokes attributed to AF, 20 to 30% of ischemic strokes are cryptogenic (no detected aetiology)
Implantable Cardiac Monitors (ILR = implantable loop recorders) have identified AF in 17 to 27.3% of these patients
Camm, Arr&Electrophys 2014; Savelieva et al., JICE 2013; Cotter et al., Neurology 2013; Etgen et al., Stroke 2013; Ritter et al., Stroke 2013; Seet et al., Circulation 2011
AF may have several clinical presentation: > 60% of patients have asymptomatic episodes
Cryptogenic stroke
new biomonitor III

## Slide 32: Case # 3: ILR in cryptogenic stroke
7 months later:
AF-episode based on ILR for 2h13m
initiation of OAC
Longer episodes are more likely to be AF
Episode PPV for any detected AF episode > 1h is > 90%
Remains subclinical AF per definition as no EKG document

## Slide 33: RM in ILRs
In ILR: RM for early detection of relevant events is critical but data is scarce
104 pts with ILR (mostly for syncope evaluation)
– retrospective observation
In RM vs. IPE (every 3 mo):
mean time from implant to diagnosis: 56 vs. 260d
targeted treatment in RM 186 days earlier
Drak-Hernàndez et al., Rev Esp Cardiol 2013

## Slide 34: Case # 4
54y, cryptogenic stroke

## Slide 35: Conclusions 1
Remote Monitoring has converged CIED follow-up to an even-based paradigm: reduces time from event to action, IPEs and follow-up burden, reduces health-care cost
RM is helpful in closely monitoring disease progression and occurrence of relevant arrythmias in HF pts
RM may reduce mortality in ICD-pts with symptomatic HF including CRT-D-patients if daily transmission, multiparameter monitoring and defined set of clinical actions
1
2
3
Multiparameter monitoring based on ICD (IN-TIME appraoch) may be considered in symptomatic HFrEF in order to improve clinical outcomes | IIb | B
Ponikowski et al., ESC guidelines on HF 2016

## Slide 36: Conclusions 2
A strategy of Remote Monitoring of CIEDs combined with at least annual IPE is recommended (Class I, LoE A)
All pts with CIEDs should be offered RM as part of standard follow-up (Class I, LoE A)
RM should be performed for surveillance of battery and lead function, reduces incidence of inappropriate shocks and allows early detection and quantification of AF
4
5
6
All ILRs should be monitored with daily automated RM
7
Slotwiner et al.: HRS Expert Consensus on Remote Monitoring, 2016

## Slide 37: Conclusions 2
A strategy of Remote Monitoring of CIEDs combined with at least annual IPE is recommended (Class I, LoE A)
All pts with CIEDs should be offered RM as part of standard follow-up (Class I, LoE A)
RM should be performed for surveillance of battery and lead function, reduces incidence of inappropriate shocks and allows early detection and quantification of AF
4
5
6
All ILRs should be monitored with daily automated RM
7
Slotwiner et al.: HRS Expert Consensus on Remote Monitoring, 2016